## Slide 1: Estimating Traffic Flow Rate on Freeways from Probe Vehicle Data and Fundamental Diagram
Khairul Anuar (PhD Candidate)
Dr. Filmon Habtemichael
Dr. Mecit Cetin (presenter)
Transportation Research Institute
Old Dominion University

## Slide 3: Introduction
Point sensors
  Aggregate data: Flow, speed, occupancy
  Relatively high cost
Probe data
  Individual vehicle trajectories (but data providers aggregate)
  Sample size might be small
  Relatively low cost
Goal: Estimate traffic flow rate from raw probe data

## Slide 4: Literature Review
Flow estimation
  Estimation of flow and density using probe vehicles with spacing measurement equipment (Seo et al, 2015)
  Deriving traffic volumes from PV data using a fundamental diagram approach (Neumann et al, 2013)
Traffic states (queue length, travel time)
  Real time traffic states estimation on arterial based on trajectory data (Hiribarren and Herrera, 2014)

## Slide 5: Objectives
Estimate traffic flow on freeways from PV data and fundamental diagram
Unique from previous studies
  Four different FDs
  Aggregation intervals of 5, 10 and 15 minutes

## Slide 6: Methodology
From FD estimate flow q when speed u is known
u is probe vehicle speed

## Slide 7: Methodology
Four different models of fundamental diagram
Model | Speed-Density Relationship | Regression
Greenshield |  | 
Underwood |  | 
Northwestern |  | 
Van Aerde |  | , , ,
Model | Speed-Density Relationship | Regression
Greenshield |  | 
Underwood |  | 
Northwestern |  | 
Van Aerde |  | 

## Slide 8: Methodology
Performance indicators
Fi is the ith estimate value
Oi is the ith observe value
n is the number of samples

## Slide 9: Case Study
Mobile Century (I-880 SF Bay area)
Probe vehicle trajectory
Study site
NB
SB
Length: 12 mile
Due to known recurring congestion, NB is analyzed
Notes: One day, Friday Feb 8, 2008. 165 drivers. GPS-enabled cell phones which on average transmitted data every 3 seconds. The penetration rate of PV is in the range of 2-5% depending on time of the day.

## Slide 10: Field Data
Probe
  Collected by 165 drivers on Friday Feb 8, 2008
  2-5% of total traffic
  GPS points @ 3-sec on average
Loop
  Speed-flow data aggregated by 5-minute intervals for about one month

## Slide 11: Speeds

## Slide 12: Case Study
Loop vs PV speed
Fundamental diagram

## Slide 13: Results
Comparison of loop detector and estimated flow from fundamental diagram

## Slide 14: Results
Distribution of percentage error for different FDs and aggregation intervals
FD models | Aggregation interval | MAPE (abs %) | RMSE (vphpl) | Avg. Error | Std. Dev.
Greenshield | 5-min | 12.5 | 189 | -2.1 | 17.1
 | 10-min | 11.1 | 169 | -2.2 | 15.2
 | 15-min | 11.1 | 168 | -2.2 | 14.7
Underwood | 5-min | 11.7 | 178 | -8.9 | 14.6
 | 10-min | 11.3 | 174 | -9.0 | 13.5
 | 15-min | 10.9 | 167 | -9.0 | 12.9
Northwestern | 5-min | 8.7 | 130 | -5.4 | 10.4
 | 10-min | 7.1 | 107 | -5.5 | 8.2
 | 15-min | 6.8 | 103 | -5.5 | 7.7
Van Aerde | 5-min | 6.4 | 98 | -2.9 | 8.1
 | 10-min | 5.3 | 83 | -3.0 | 6.2
 | 15-min | 5.2 | 79 | -3.0 | 6.2

## Slide 15: Conclusions
Van Aerde provides the best result
Higher accuracies as aggregation interval increases
Estimates are more accurate during congestion rather than free-flow

## Slide 16: Future Work
Focus on congestion period
Utilize shockwave theory to identify additional traffic state
Other sites

## Slide 17: Questions?
Funded by Mid-Atlantic Transportation Sustainability Center – Region 3 University Transportation Center